## Slide 1: Making the most of Solid State Disk in Oracle 11g
Guy Harrison
Director, R&D Melbourne
Email: guy.harrison@quest.com
Twitter: @guyharrison
Web: http://www.guyharrison.net

## Slide 2: Introductions
Notes: Apologies, I’m a database type.....
Quest is best known for toad, but we also have enterprise monitoring across all levels of the stack
In Melbourne, SQL Navigator + the spotlights.
It’s not a complete co-incidence about the star trek theme.

## Slide 3
Notes: Insanely popular – literally millions of users

## Slide 5: Agenda
Brief History of Magnetic Disk
Solid State Disk (SSD) technologies
SSD internals
Oracle DB flash cache architecture
Performance comparisons
Recommendations and Suggestions

## Slide 6
A brief history of disk

## Slide 7: 5MB HDD circa 1956

## Slide 8: 28MB HDD - 1961
1800 RPM

## Slide 9: The more that things change....

## Slide 10: Moore’s law
Transistor density doubles every 18 months
Exponential growth is observed in most electronic components:
  CPU clock speeds
  RAM
  Hard Disk Drive storage density
But not in mechanical components
  Service time (Seek latency) – limited by actuator arm speed and disk circumference
  Throughput (rotational latency) – limited by speed of rotation, circumference and data density

## Slide 11: Disk trends 2001-2009
Chart: %age change
| IO Rate | Disk Capacity | IO/Capacity | CPU | IO/CPU
Pct | 259.5205 | 1634.8774 | -629.9609 | 1013.3333 | -390.4638

## Slide 12
Solid State Disk

## Slide 13: SSD to the rescue?
Chart: Seek time (us)
| Magnetic Disk | SSD SATA Flash | SSD PCI flash | SSD DDR-RAM
microseconds | 4000 | 80 | 25 | 15
Column2
Column3

## Slide 14: Power consumption
Chart: Watts (logarithmic scale)
| Idle | Seek | Start up
SATA HDD | 8 | 10 | 20
Flash SSD | 0.08 | 0.15 | 0

## Slide 15: Economics of SSD
Chart: $/IOP
| Seagate SATA HDD | Seagate SAS HDD | Intel MLC SATA SSD | Intel SLC SATA SSD | FusionIO PCI MLC Duo SSD | FusionIO PCI SLC SSD
$/IOP | 2.38 | 1.53 | 0.04675 | 0.0525 | 0.058425 | 0.061071
$/GB | 0.091146 | 1 | 6.875 | 21.875 | 24.9219 | 53.4375
$/GB
$/IOPS

## Slide 16: Tiered storage management
Main Memory
DDR SSD
Flash SSD
Fast Disk (SAS, RAID 0+1)
Tape, Flat Files, Hadoop
Slow Disk (SATA, RAID 5)
$/IOP
$/GB

## Slide 17: Storage Tiering
Storage Tiering For Dummies,® Oracle Special Edition, Wiley 2011

## Slide 18
SSD technology and internals

## Slide 19: Flavours of Flash SSD
DDR RAM Drive
SATA flash drive
PCI flash drive
SSD storage Server

## Slide 20: PCI SSD vs SATA SSD
PCI vs SATA
  SATA was designed for traditional disk drives with high latencies
  PCI is designed for high speed devices
  PCI SSD has latency ~ 1/3rd of SATA

## Slide 21
Booth 1107

## Slide 22: Flash SSD Technology
Storage Hierarchy:
Cell: One (SLC) or Two (MLC) bits
Page: Typically 4K
Block: Typically 128-512K
Writes:
Read and first write require single page IO
Overwriting a page requires an erase & overwrite of the block
Write endurance:
100,000 erase cycles for SLC before failure
5,000 – 10,000 erase cycles for MLC

## Slide 23: Flash SSD performance
Chart: Microseconds
| Read (4k page seek) | First insert (4k page write) | Update (256K block erase)
Microseconds | 25 | 250 | 2000

## Slide 24: Flash Disk write degradation
All Blocks empty:
  Write time=250 us
25% part full:
  Write time= ( ¾ * 250 us + 1/4 * 2000 us) = 687 us
75% part full
  Write time = ( ¼ * 250 us + ¾ * 2000 us ) = 1562 us
Empty
Partially Full

## Slide 25: Data Insert
Valid Data Page
Empty Data Page
InValid Data Page
Free Block Pool
Used Block Pool
SSD Controller
Insert

## Slide 26: Data Update
Valid Data Page
Empty Data Page
Invalid Data Page
Free Block Pool
Used Block Pool
SSD Controller
Update

## Slide 27: Garbage Collection
Valid Data Page
Empty Data Page
Invalid Data Page
Free Block Pool
Used Block Pool
SSD Controller

## Slide 29
11g DB flash Cache

## Slide 30: Oracle DB flash cache
Introduced in 11gR2 for OEL and Solaris only
Secondary cache maintained by the DBWR, but only when idle cycles permit
Architecture is tolerant of poor flash write performance

## Slide 31
Buffer cache and Free buffer waits
Database
files
Buffer
cache
DBWR
Oracle process
Free
Buffer
Waits
Write dirty blocks to disk
Write to buffer cache
Read from disk
Read from buffer cache
Free buffer waits often occur when reads are much faster than writes....

## Slide 32
Flash Cache
Database
files
Buffer
cache
DBWR
Oracle process
Write dirty blocks to disk
Write to buffer cache
Read from disk
Read from buffer cache
Flash Cache
Write clean blocks (time permitting)
Read from flash cache
DB Flash cache architecture is designed to accelerate buffered reads

## Slide 33: Configuration
Create filesystem from flash device
Set DB_FLASH_CACHE_FILE and DB_FLASH_CACHE_SIZE.
Consider Filesystemio_options=setall

## Slide 34: Flash KEEP pool
You can prioritise blocks for important objects using the FLASH_CACHE clause:

## Slide 35: Oracle Db flash cache statistics
http://guyharrison.squarespace.com/storage/flash_insert_stats.sql

## Slide 36: Flash Cache Efficiency
http://guyharrison.squarespace.com/storage/flash_time_savings.sql

## Slide 37: Flash cache Contents
http://guyharrison.squarespace.com/storage/flashContents.sql

## Slide 38
Performance tests

## Slide 39: Test systems
Low end system:
  Dell Optiplex dual-core 4GB RAM
  2xSeagate 7500RPM Baracuda SATA HDD
  Intel X-25E SLC SATA SSD
Higher end system:
  Dell R510 2xquad core, 32 GB RAM
  4x300GB 15K RPM,6Gbps Dell SAS HDD
  1xFusionIO ioDrive SLC PCI SSD

## Slide 40: Performance: indexed reads(X-25)
Chart: Elapsed (s)
| No Flash | Flash cache | Flash tablespace
CPU | 36.96 | 37.64 | 34.85
db file IO | 487.73 | 99.74 | 17.14
flash cache IO | 0 | 8.4
Other | 5.01 | 0 | 0
Total | 529.7 | 143.27 | 48.17

## Slide 41: Performance: Read/Write (X-25)
Chart: Elapsed time (s)
| No Flash | Flash Cache | Flash tablespace
CPU | 29.19 | 22.75 | 26.5
db file IO | 2722.2 | 706.97 | 103.85
write complete | 359.05 | 50.29 | 37.43
free buffer | 156.81 | 869.38 | 36.62
flash cache IO | 0 | 3.05
Other | 21.76 | 40.67 | 0
Total | 3289.01 | 1693.11 | 199.59
Notes: The higher logical read rate overwhelms the HDD

## Slide 42: Random reads – FusionIO
Chart: Elapsed time (s)
| SAS disk, no flash cache | SAS disk, flash cache | Table on SSD
CPU | 112.9568 | 77.1233 | 62.8254
Other | 4.4947 | 1.2156 | 0.19292
DB File IO | 2092.5597 | 440.9082 | 57.8436
Flash cache IO | 0.56892 | 63.6513 | 0.13239
Total | 2210.5801 | 582.8985 | 120.9944

## Slide 43: Updates – Fusion IO
Chart: Elapsed Time (s)
| SAS disk, no flash cache | SAS disk, flash cache | Table on SSD
DB CPU | 419.4402 | 400.2091 | 418.2284
db file IO | 5691.3961 | 1223.4634 | 75.2586
log file IO | 93.6371 | 169.056 | 33.119
flash cache | 0.77048 | 94.8516 | 0.35203
free buffer waits | 0 | 19.151 | 0
Other | 13.5246 | 27.0867 | 1.8298
Total | 6218.7685 | 1933.8179 | 528.7878

## Slide 44: Full table scan – FusionIO
Chart: Elasped time (s)
| SAS disk, no flash cache | SAS disk, flash cache | Table on SSD
CPU | 79.3289 | 78.736 | 63.0494
Other | 1.9e-05 | 0.000258 | 6.7e-05
DB File IO | 338.7691 | 319.6205 | 9.1661
Flash Cache IO | 0 | 0 | 0
Total | 418.098 | 398.3568 | 72.2156

## Slide 45: Sorting – what we expect
Chart: PGA Memory available (MB)
| 300 | 250 | 200 | 175 | 150 | 125 | 100 | 75 | 50 | 32 | 16 | 8 | 4 | 3 | 2 | 1
Table/Index IO | 1.6429 | 1.918 | 1.9394 | 1.9761 | 1.6666 | 1.8055 | 2.01 | 2.4684 | 2.4741 | 1.9923 | 2.2099 | 2.6604 | 2.1165 | 2.8589 | 1.6288 | 2.8069
CPU Time | 2.4375 | 2.3438 | 2.6875 | 2.6406 | 2.7969 | 2.5312 | 3.1719 | 2.9062 | 3.2656 | 3.1562 | 2.9531 | 3.6562 | 3.7969 | 4.1562 | 4.25 | 5.6094
Temp Segment IO | 0.020427 | 0.020415 | 0.018127 | 0.020452 | 0.012464 | 0.02249 | 12.9389 | 14.5505 | 12.9073 | 13.8224 | 14.4851 | 16.1391 | 25.0068 | 34.2593 | 54.4227 | 84.2552
Memory Sort
Single Pass
Disk Sort
Multi-pass
Disk Sort

## Slide 46: Disk Sorts – temporary tablespace
Chart: Sort Area Size
| 7 | 10 | 19 | 33 | 48 | 76 | 95 | 191 | 286
SAS based TTS | 3587.309 | 3462.82 | 2318.5778 | 1262.0966 | 708.7546 | 540.8165 | 529.5764 | 387.0673 | 452.4194
SSD based TTS | 552.2839 | 539.4331 | 464.4804 | 438.6057 | 425.5075 | 403.9703 | 393.5929 | 282.0677 | 304.2268
Single Pass
Disk Sort
Multi-pass
Disk Sort

## Slide 47: Redo performance – Fusion IO
Chart: Elapsed time (s)
| SAS based redo log | Flash based redo log
CPU | 185.4458 | 185.7698
Log IO | 106.9489 | 106.1647
Total | 292.3947 | 291.9345

## Slide 48: Concurrent redo workload (x10)
Chart: Elapsed time (s)
| SAS based redo log | Flash based redo log
CPU | 1605.4569 | 1637.1261
Other | 396.5898 | 330.8391
Log File IO | 1943.9343 | 1681.4226

## Slide 49: Buffer Cache bottlenecks
Flash cache architecture avoids ‘free buffer waits’ due to flash IO, but write complete waits can still occur on hot blocks.
Free buffer waits are still likely against the database files, due to high physical read rates created by the flash cache

## Slide 50: Write degradation
In theory, high sustained write IO can lead to SSD degradation when GC fails to cope with the block erase/update cycle
In practice, this is rarely noticeable from Oracle:
  Oracle write IO is largely asynchronous (DBWR)
  Almost all write activity has at least an equal amount of read activity
  Garbage collection and wear levelling algorithms are sophisticated in decent SSD drives

## Slide 53: Fusion IO direct cache
Read-intensive, potentially massive tablespaces
Temp Tablespace
Hot Segments
Hot Partitions
DB Flash Cache
(limited to the size of the SSD)
Regular Block Device
ioMemory VSL
File System/ Raw Devices/ ASM
directCache
File System/ Raw Devices/ ASM
Caching Block Device
ioMemory VSL
LUN

## Slide 54: Fusion IO direct cache – Table scans
Chart: Elapsed time (s)
| No cache 1st scan | No cache 2nd scan | direct cache on 1st scan | direct cache on 2nd scan
CPU | 40.5538 | 40.4848 | 41.6247 | 32.0891
IO | 106.277 | 106.3897 | 105.2769 | 4.3867
Other | 0 | 0 | 0
Total | 146.8308 | 146.8745 | 146.9015 | 36.4758

## Slide 55
Exadata

## Slide 57: Exadata flash storage
4x96GB PCI Flash drives on each storage server
Flash can be configured as:
  Exadata Smart Flash Cache (ESFC)
  Solid State Disk available to ASM disk groups
ESFC is not the same as the DB flash cache:
  Maintained by cellsrv, not DBWR
  DOES support full table scans
  DOES NOT support smart scans
    Unless CELL_FLASH_CACHE= KEEP,
  Statistics accessed via the cellcli program
Considerations for cache vs. SSD are similar

## Slide 58: Exadata: Flash grid disk vs ESFC
Chart: Seconds
| SAS disk no flash cache | SAS disk with flash cache | SSD disks (no flash cache)
IO | 1184.9031 | 393.1396 | 89.5906
CPU | 54.6267 | 36.0815 | 29.5035
Total | 1239.5298 | 429.2211 | 119.0941
100M row table, 200,000 random PK lookups, 1M possible keys

## Slide 59: Exadata: SSD disk for Redo
Chart: Elapsed time (s)
| SAS redo 10 concurrent (avg) | SSD redo 10 concurrent (avg) | SAS redo 1 concurrent | SSD redo 1 concurrent
DB CPU | 73.1668 | 82.6978 | 72.203 | 75.4045
Log IO | 278.9623 | 6801.8525 | 163.3763 | 931.4041
Other | 0.080763 | 0.071564 | 0.003775 | 0.006529
Total | 352.2099 | 6884.6219 | 235.5831 | 1006.8151

## Slide 60
Summary

## Slide 61: Recommendations
Don’t wait for SSD to become as cheap as HDD
  Magnetic HDD will always be cheaper per GB, SSD cheaper per IO
Consider a mixed or tiered storage strategy
  Using DB flash cache, selective SSD tablespaces or partitions
  Use SSD where your IO bottleneck is greatest and SSD advantage is significant
DB flash cache offers an easy way to leverage SSD for OLTP workloads, but has few advantages for OLAP or Data Warehouse

## Slide 62: How to use SSD
Database flash cache
  If your bottleneck is single block (indexed reads) and you are on OEL or Solaris 11GR2
Flash tablespace
  Optimize read/writes against “hot” segments or partitions
Flash temp tablespace
  If multi-pass disk sorts or hash joins are your bottleneck
FusionIO direct cache
  If you want to optimize both scans and index reads OR you are not on OEL/Solaris 11GR2

## Slide 65: References
Latest version of this presentation:
  http://www.slideshare.net/gharriso/ssd-and-the-db-flash-cache
Quest whitepaper:
  http://www.quest.com/documents/landing.aspx?id=15423
Guy’s SSD guide
    http://guyharrison.squarespace.com/ssdguide/